## Slide 1: Towards Devising a Vibration Based Machinery Health Monitoring System
Department of Textile Machinery Design and Maintenance
Bangladesh University of Textiles, Dhaka, Bangladesh
Md. Harunur Rashid Bhuiyan, Iftekhar Morshed Arafat, Masfiqur Rahaman,
Tarik Reza Toha, and Shaikh Md. Mominul Alam
Paper ID: MATPR-D-21-07129
ICCAME 2021

## Slide 2: Outline
Textile industry
Background and motivation
Our proposed system
  System design
  System implementation
Experimental evaluation
  Industrial data collection
  Findings
Conclusion and future work

## Slide 3: Textile Industry
Chart: 
| Knitware | Woven garments | Frozen food | Agricultural products | Chemical products | Jute & Jute mfd | Specialized textiles | Engineering products | Others
 | 0.4001 | 0.3711 | 0.0275 | 0.015 | 0.0063 | 0.0454 | 0.0115 | 0.0192 | 0.0756

## Slide 4: Background
Excess vibration for a long period of time can cause deterioration of machine parts [1].
Too much vibration thus can reduce machine lifetime in the long run
These deteriorations in long term can cause breakage in machine parts
An inboard bearing nearly destroyed due to excessive vibration

## Slide 5: Motivation of our research
Monitoring the machine vibration to get an early warning about scheduled maintenance
Finding a standard vibration amount for each machine to detect any change in machine’s structural integrity
Making the system wireless so that it is suitable for industry
Vibration analysis for scheduled maintenance

## Slide 6: Related Work
A machine maintenance system based on machine tool condition [3]
  Rastegari et al., RAMS, 2017
  Monitor the vibration of spindle units of machine.
  Uses Ethernet for data transmission that is expensive and not suitable for industrial application.
A Wi-Fi based periodic vibration monitoring of pump [4]
  Lewis et al., Proceedings of the 33rd International Pump Users Symposium. Turbo-machinery Laboratory, 2017
  It does the periodic vibration monitoring in the pump
  There is no Wi-Fi in the production areas
FEM-based damage assessment through vibration monitoring [5]
  A Cabboi et al., Journal of Construction and Building Materials, Elsevier, 2017
  Uses fiber optic cable for data transmission.
  Impracticable solution for textile industry

## Slide 7: Our Contribution
We propose a low-cost and wireless vibration monitoring system comprising off-the-shelf hardware resources and Bluetooth modules, which is applicable to the textile industry

## Slide 8: Operational Block Diagram
Bluetooth module
Controller module (Arduino UNO) [Sender]
Sensor module (Vibration sensor SW-420)
Power module
Real time clock
Smart phone
Controller module (Arduino UNO) [Receiver]
Bluetooth module
Power module
Storage module
Bluetooth module

## Slide 9: System Implementation
Sender Unit
Receiver Unit
SW-420 Vibration sensor
HC-05 Bluetooth module
Arduino Uno R3
DS-3231 clock module
Breadboard
HC-05 Bluetooth module
SD card module
Arduino Uno R3
Jumper wire
Breadboard

## Slide 10: Industrial Data Collection
Soft winding section
(Gangeetal Thread Factory)
Spinning section (R.K. Textiles)

## Slide 11: Industrial Data Collection (contd.)
Chart: No of readings

## Slide 12: Industrial Data Collection (contd.)
Chart: No of readings

## Slide 13: Industrial Data Collection (contd.)
Chart: No of readings
Chart: No of readings

## Slide 14: Industrial Data Collection (contd.)
Chart: Output signal level (ms)
| Soft winding machine(2 years, bad quality) | Soft winding machine(7 years, good quality) | Soft winding machine(2 years, good quality)

 | 5.3563 | 1.3496 | 0.078352
The soft winding machine (used for 2 years, good structural integrity) has the least amount of vibration.
Machine’s structural integrity has higher impact on the vibration level than the age of the machine.
So, by looking at the vibration amount of a machine and comparing it with its general vibration amount we can determine its health condition and quality

## Slide 15: Industrial Data Collection (contd.)
Chart: Utility section
| Boiler 1 | Boiler 2 | Generator 1 | Generator 2
 | 1.6085 | 0.88532 | 6.0111 | 4.4575
Chart: Production section
| Auto Coner | Ring Spinning machine | Carding machine | Knitting machine 1 | Knitting machine 2
 | 8.3146 | 23.7188 | 6.1126 | 0.86119 | 1.1733
The generators in utility and the ring spinning machine has most vibration. And they need the most maintenance

## Slide 16: Conclusion and Future Work
Existing vibration monitoring systems are generally costly and less suitable for textile industry
We propose a low-cost, wireless and easy-to-implement vibration monitoring device for textile industry
In the future, we plan to scale-up our system and evaluate it in a realistic setting

## Slide 17: References
S. Ahilan, M. Hemkumar, N. Mishra, Vibration analysis of vertical pumps, Indian Journal of Scientific Research (2018) 251–257.
Vibration study and root cause analysis, hydro inc., https:// hydroinc.com/ blog/ 2009/ 12/01/vibration-study-root-cause-analysis/
A. Rastegari, A. Archenti, M. Mobin, Condition based maintenance of machine tools: Vibration monitoring of spindle units, in: 2017 Annual Reliability and Maintainability Symposium (RAMS), IEEE, 2017, pp. 1–6.
B. Lewis, M. Miller, et al., Predictive diagnostics for pump seals: Field trial learnings, in: Proceedings of the 33rd International Pump Users Symposium, Turbomachinery Laboratory, Texas A&M Engineering Experiment Station, 2017.
A. Cabboi, C. Gentile, A. Saisi, From continuous vibration monitoring to fem-based damage assessment: application on a stone-masonry tower, Construction and Building Materials 156 (2017) 252–265.

## Slide 18: Thank You!
Questions are welcome!
Email: harunurrashidmoon@gmail.com